## Slide 1
Microprocessor & Computer Architecture (μpCA)
UE19CS252
Laboratory / Hands-on Plug – in Programs

## Slide 2
ARMSIM EMBEST BOARD PLUGIN PROGRAMS
1. LED Light Up
2. Seven Segment Display
3. Move a string from Right to Left on LCD
(40 columns by 15 rows)

## Slide 3
SWI Operations for EMBEST BOARD Plug‐Ins:
The SWI codes numbered greater than 255 have special purposes.
They are mainly used for interaction with Plug‐in modules which can be loaded with the ARMSim# simulator.
The use of “EQU” is strongly advised to substitute the actual numerical code values. Examples of code is also provided at the end of the section.
The default installation of ARMSim# comes with two Plug‐ins module extensions: SWIInstructions and EmbestBoard.
Important Note: All Plug‐ins have to be enabled explicitly by checking their option in the File > Preferences menu and selecting the appropriate line from within the tab labelled Plugins.

## Slide 4
Instructions to run the plug-in codes
Install ARMSIM simulator
Go to File-->Preferences->Plugins and select "Embest Board Plugin"
Go to view-->PluginsUI
Run the code(File Load-Select the program written in notepad file with extension .s

## Slide 5
There are 5 main components in this view available for programming:
One 8‐segment display (output).
Two red LED lights (output).
Two black buttons (input).
Sixteen blue buttons arranged in a keyboard 4 x 4 grid (input).
One LCD display screen, which is a grid of 40 columns by 15 rows of individual cells. The coordinates for each LCD cell are specified by a {column, row} pair. The top‐left cell has coordinates {0,0},while the bottom‐right cell has coordinates {39,14}. Each cell can contain exactly one ASCII character.
EMBEST BOARD View

## Slide 6
EMBEST BOARD View

## Slide 7
SWI Codes used in PROGRAM 1 : Set the LED to light up: LED Light Up.s

## Slide 9
.text
mov r0, #0
loop: swi 0x201 ; to light up LED , r0= 1 means right led light up, r0=2 means left
; LED and r0=3 means both LED light up
add r0, r0, #1
mov r4, #64000
delay: sub r4, r4,#1
cmp r4, #0
bne delay
cmp r0, #3
ble loop
.end
PROGRAM 1 - Set the LED to light up: LED Light Up.s

## Slide 10
PROGRAM 2

## Slide 12
; Program to display 0 to F and F-0 on the 8 segment display depending
; on the which black button is pressed
.text
.global _start
begin: mov r0, #0
mov r2,#0
again: swi 0x202 ; check whether
; black button pressed or not
cmp r0, #1
beq loop1
PROGRAM 2 Display 0-9,A-F on an 8 segment display
cmp r0, #2
beq loop2
b again
loop1: mov r5,#16
ldr r1,=zero

## Slide 13
back1: ldrb r0, [r1]
swi 0x200 ; Set 8 segment display to light up
bl delay
add r1,r1,#1
sub r5, r5,#1
cmp r5, #0
bne back1
b again
loop2: mov r5,#16
ldr r1,=F
back2: ldrb r0, [r1]
swi 0x200 ; Set 8 segment
; display to light up
bl delay
sub r1, r1, #1
sub r5, r5,#1
cmp r5, #0
bne back2
b again
PROGRAM 2 Display 0-9,A-F on an 8 segment display

## Slide 14
delay: mov r4, #64000
loop3: sub r4, r4, #1
cmp r4, #0
bge loop3
mov pc, lr
.data
zero: .byte 0b11101101
one: .byte 0b01100000
two: .byte 0b01101110
three: .byte 0b11111010
four: .byte 0b00110011
five: .byte 0b10101011
six: .byte 0b10101111
seven: .byte 0b01110000
eight: .byte 0b11101111
nine: .byte 0b11100011
A: .byte 0b11100111
B: .byte 0b00101111
C: .byte 0b10001101
D: .byte 0b01101110
E: .byte 0b10001111
F: .byte 0b10000111
PROGRAM 2 Display 0-9,A-F on an 8 segment display

## Slide 15
The appropriate segments light up to display a number or a character. The pattern of segments to be lit up is assigned to register R0 before the call to swi 0x200.
For example, to display the number “3”, segments “A”, “B”, “C”, “D” and “F”must be illuminated. The code to be assigned to R0 is computed by the logical OR of the individual byte codes.
PROGRAM 2 : Set the 8‐Segment Display to lightup

## Slide 16
PROGRAM 2 - Set the 8‐Segment Display to light up: Eight Segment .s

## Slide 17
The “.equ” statements are useful for accessing the byte values associated with the labels of each segment as shown in Figure.
The byte values representing a particular number are already “ORed” together within the array data structure and can be indexed appropriately.
It may be easier to use a data declaration for an array of words and then index into it. Each element can be initialized to contain the value representing a number by having the appropriate byte values “ORed” together.

## Slide 22
; Streaming right to left
.text
mov r0 , #30 ; r0 = x
mov r1 , #7 ; r1 = y
mov r7 , #0
ldr r8 , =num
ldr r8 , [r8]
ldr r2 , =str
loop: swi 0x204 ; display a string on screen address should be in r2 reg
PROGRAM 3 Move a string left to right ,right to left on LCD in Embest Board
bl sum
cmp r0 , #0
subne r0 , r0 , #1
swieq 0x11
b loop

## Slide 23
sum: cmp r7 , r8
addne r7 , r7 , #1
bne sum
swi 0x206 ;Clear one line in the display on the LCD screen.r0-line no(y)
mov r7 , #0
mov pc , lr
.data
str: .asciz "HELLO WORLD"
num: .word 15000
PROGRAM 3 Move a string left to right ,right to left on LCD in Embest Board

## Slide 24
Keyboard - Interface

## Slide 25
THANK YOU
Team MPCA
Department of Computer Science and Engineering